## Slide 1
SPIE Photonics Europe
Strasbourg 29 March - 2 April 2020
Digital Forum 6-10 April 2020
New perspectives
in Correlation Plenoptic Imaging
Francesco V. Pepe
Università degli Studi di Bari, Italy
Istituto Nazionale di Fisica Nucleare (INFN) – Sezione di Bari, Italy
francesco.pepe@ba.infn.it
in collaboration with
F. Di Lena, M. D’Angelo, A. Garuccio, A. Scagliola
G. Scala, S. Pascazio (Univ. Bari)
G. Scarcelli (Univ. Maryland, College Park)

## Slide 2
Optical imaging
Figures of merit: resolution, depth of field, signal-to-noise ratio (SNR), aberration correction/limitation
but…
Resolution vs depth of field
Depth of field vs SNR
SNR vs aberrations
Resolution vs aberrations
in correlation imaging: resolution vs SNR
TRADEOFFS
Relevant parameters:
Focal length f
Numerical aperture D/2f
Light wavelength λ

## Slide 3
Plenoptic imaging
Microlens
array
Combined imaging of the object and the main lens to reconstruct the direction of light → DOF increase, refocusing, change of point of view, 3D reconstruction in post processing
Depth of field is increased without losing signal-to-noise ratio…
From lytro.com (discontinued)
Lippman (1908), Adelson and Wang (1992)
Ng (2005)

## Slide 4
Plenoptic imaging
Microlens
array
… however spatial resolution is reduced by a factor coinciding with directional resolution
From lytro.com (discontinued)
Combined imaging of the object and the main lens to reconstruct the direction of light → DOF increase, refocusing, change of point of view, 3D reconstruction in post processing
Lippman (1908), Adelson and Wang (1992)
Ng (2005)

## Slide 5
Plenoptic imaging: applications
Use of image reconstruction or deconvolution techniques to recover lost resolution

## Slide 6
Correlation Plenoptic Imaging: principle
Main idea: use correlation imaging to avoid resolution loss
Propagate two correlated light beams; at least one of them interacts with the object
Follow in time the intensitites at their ends with two spatially resolving detectors Da and Db
Time-average to evaluate point-to-point correlations of intensity fluctuations
D’Angelo et al, PRL 116, 223602 (2016)
Patent IT102016000027106 (2016)

## Slide 7
Correlation Plenoptic Imaging: first realization
Combined to refocus and change point of view
Measurement
Summing correlations over Db yields the incoherent ghost image of the object
Focused only if
Multiple images of the object detected by the sensor Da (one for each pixel of Db)

## Slide 8
Correlation Plenoptic Imaging: first realization
Ghost image
Refocused image
Pepe et al, PRL 119, 243602 (2017)

## Slide 9
Correlation Plenoptic Imaging: first realization
Ghost image
Refocused image
Drawbacks:
Low SNR: inherits the typical resolution-SNR tradeoff of ghost imaging → no p.o.v. change!
Impossibility to monitor the object in real time
Pepe et al, PRL 119, 243602 (2017)

## Slide 10
The image of the object (not necessarily focused) is formed on Da by an ordinary lens.
Db detects the focused ghost image of the lens. This enables to reconstruct and select the direction of light.
Measurement
CPI: an alternative architecture
Advantages:
Higher SNR: noise is not negatively affected by spatial resolution
The scene can be observed even by direct intensity measurement (with no refocusing)
Pepe et al, J. Opt. 19, 114001 (2017)
Scala et al, PRA 99, 053808 (2019)
Pat. appl. PCT/IB2017/055842 (2017)

## Slide 11
General limitations of CPI
In these setups, the direction of light before and after the object must change in a predictable way: transmission, mirror-like reflection.
This condition rules out relevant categories for microscopy:
Diffusive objects
Objects surrounded by a scattering medium or turbulence
Randomly emitting samples (e.g. fluorescent)

## Slide 12
The Correlation Plenoptic Microscope
Ordinary microscope: sample in the focal plane of an objective (O) of focal length fO, sensor in the focal plane of a tube lens (T) of focal length fT
Magnification:
Emitted intensity profile
Arbitrary sample distance
Focused case

## Slide 13
The Correlation Plenoptic Microscope
Correlation Plenoptic Microscope: correlated imaging of the objective focal plane and of the objective surface
Emitted intensity profile
Arbitrary sample distance f
Intensity correlator
D’Angelo, Di Lena, Garuccio, Pepe, Scagliola, patent appl. IT102018000007857 (2018),
Paper on theory under peer review; paper on experiment in preparation.

## Slide 14
CPM: change of point of view
Geometrical-optics limit
The transverse shift of the image depends on the selected point of the objective surface and on the longitudinal distance f from the objective
OBJECTIVE LENS
SAMPLE

## Slide 15
CPM: change of point of view
Out-of-focus triple slit
(planar object)
Center-to-center slit distance:
d =39.37 μm
Objective focal length: fO = 25.6 mm
Tube focal length: fT = 175.0 mm
Object distance: f = 24.5 mm
Number of frames: Nfr = 30k
9 panels
9 points on the objective
9 points of view

## Slide 16
CPM: change of point of view
Starch aggregates dispersed in gel (3D sample)
Objective focal length: fO = 25.6 mm
Tube focal length: fT = 175.0 mm
Number of frames: Nfr = 30k
Detail recovery
3D rendering
- 4.17 mm - 1.39 mm 1.39 mm 4.17 mm
Scagliola et al, in preparation

## Slide 17
CPM: refocusing
Refocusing algorithm based on the geometrical-optics properties of
Standard image
REFOCUSING
CASE
A
CASE
B
Center-to-center slit distance: d = 39.37 μm
Distance from focal plane: f – fO = – 1.1 mm
Center-to-center slit distance: d = 39.37 μm
Distance from focal plane: f – fO = + 1.1 mm
distance from focal plane [mm]

## Slide 18
CPM: refocusing
Refocusing algorithm based on the geometrical-optics properties of
Starch sample
Refocused plane variation

## Slide 19
CPM: refocusing
Refocusing algorithm based on the geometrical-optics properties of
Section of bovine cornea: birefringent collagen fibers
Focused image
100 μm out of focus
Refocusing
60 μm

## Slide 20
CPI between arbitrary planes
Francesco Di Lena, PhD thesis (2019)
Patent application PCT/IB2019/052351 (2019)
Single-lens CPI device
The lens focuses two different planes inside a 3D object on Da and Db
CPI refocusing

## Slide 21
CPI between arbitrary planes
Francesco Di Lena, PhD thesis (2019)
E. De Scisciolo et al. Int. J. Quantum Inf. (2020)
Entangled photon illumination
Work in progress on:
Theory: SNR, investigation of different correlation protocols (e.g. differential correlation imaging)
Experiment: noise reduction factor (found <1), refocusing
Collaboration with
A. Avella and I. Ruo-Berchera (INRIM)

## Slide 22
Other perspectives
Scientific-technological challenges toward real-world applications:
Improvement of SNR by optimizing setups, sources and correlation measurement protocols
Reduction of detection times (SPAD arrays as ultrafast detectors, use of compressive sensing techniques, …)
Superresolution
Application testbeds:
Biomedical samples
Imaging from/of space
…
SUPPORT:
PICS – Plenoptic Imaging with Correlations: young researcher grant of INFN (2017-2019)
CLOSE – Close to Earth: PON ARS project of the Italian Ministry of Education, University and Research (2019-)

## Slide 23
QuOT Lab+Theory group @ UniBA
Students :
  Davide Giannella, Alessandro Lupo
  Emiliana De Scisciolo, Francesco Di Lena, Aldo Mazzilli
  Giovanni Scala
Researchers:
  Alessio Scagliola
  Gianlorenzo Massaro
  Francesco V. Pepe
  Milena D'Angelo
  Augusto Garuccio
Collaborations:
Univ. Maryland (USA)
INRIM Torino (IT)
EPFL (CH)
Planetek (IT/GR)
Univ. Olomouc (CZ)
Contact:
milena.dangelo@uniba.it
Qu3D
PICS
PICS4ME